## Slide 2: Digital technology
TK1104-1 22H
Lecturer: Toktam Ramezanifarkhani
Toktam.Ramezanifarkhani@kristiania.no
Toktamr@ifi.uio.no

## Slide 3
Hardware-Computer Organization

## Slide 4: So far
Generally
  First Abstraction level, computer defintion
  Digital vs analog, Harware, Software
Computation in computer
  Binary system
Computer Arch.
  Gates, digtal circutes
TYPES: Analog vs. Digital, Continuous vs. Discrete, Specialized vs. General, Electronic vs. Mechanical
  https://www.youtube.com/watch?v=btgAUdbj85E&t=10s
  https://www.youtube.com/watch?v=L_j8wlm2NKA

## Slide 5: Today
Instructions and programming based on CPU
  Structure, Register, IPOS
Construction of (IBM) PC systems.
  Not the only ones, previous lecture.
  Not looking at EVERYTHING.
  Hopefully some of the most important
Most important
  Understand context
  Not all components in detail,
    but what type they are &
    How they relate to the rest

## Slide 6: The motherboard

## Slide 7: Motherboard
Connects:
  CPU
  Chipset
  Buses
  Memory tracks and RAM
  Expansion slots and extra cards
  Gates and «plugs»
a set of electronic components in an integrated circuit known as a "Data Flow Management System" that manages the data flow between the processor, memory and peripherals
Notes: the term chipset commonly refers to a set of specialized chips on a computer's motherboard
https://www.tomshardware.com/reviews/motherboard-parts-explained,5669.html

## Slide 8: Modern Motherboard: Connectors, Ports & Chipsets
1. CPU socket | 2. Chipset | 3. DIMM/RAM slots
4. PCIe x16 slot | 5. PCI x1 slot | 6. M.2 connector
7. SATA ports | 8. Front panel connectors | 9. USB 2. header
10. USB 3.1 Gen1 header | 11. USB 3.1 Gen2 header | 12. ATX power connector
13. CPU power connector | 14. BIOS chips | 15. CMOS battery
16. Fan headers | 17. Front panel header | 18. VRM heatsink
19. COM/Serial header | 20. TPM header | 21. RGB header
Asus Prime X470-Pro
DIMM (dual in-line memory module) slots are the place on your motherboard where the RAM goes
A PCIe x1 slot has one lane and can move one bit per cycle
X16 ideal for large and power hungry cards like a graphics card
To connect hard drives to motherboards
a ROM chip found on motherboards that allows you to access and set up your computer system at the most basic level
The BIOS is the program that starts a computer up, and the CMOS is where the BIOS stores the date, time, and system configuration details it needs to start the computer. ... CMOS is a type of memory technology, but most people use the term to refer to the chip that stores variable data for startup.
Voltage Regulator Thermal Module Pad
Notes: https://www.tomshardware.com/reviews/motherboard-parts-explained,5669.html
CMOS stands for “Complementary Metal Oxide Semiconductor.” The CMOS battery powers the BIOS firmware in your laptop [2]. BIOS needs to remain operational even when your computer isn't plugged into a power source. ... When your computer gets unplugged, BIOS relies on the CMOS battery for power.
COM (communication port) is the original, yet still common, name of the serial port interface on PC-compatible computers. It can refer not only to physical ports, but also to emulated ports, such as ports created by Bluetooth or USB adapters.

## Slide 9: Different USBs
https://www.youtube.com/watch?v=dERa_bMDvcg

## Slide 10: Rear Ports
22. PS/2 Keyboard/Mouse port | 23. USB 3.0/3.1 Gen1 ports
24. DisplayPort | 25. HDMI port
26. USB Type-C | 27. USB 3.1 Gen2
28. Ethernet port | 29. Analogue/digital audio ports
High-Definition Multimedia Interface (HDMI) is an audio/video interface for transmitting uncompressed video data and compressed or uncompressed digital audio data from an HDMI-compliant source device, such as a display controller, to a compatible computer monitor, video projector, digital television, or digital audio device.

## Slide 11: Form factor
The form factor defines the physical size, design and to some extent available functionality on the motherboard.
ATX (12"x9.6")
    Expansion grooves on the wide edge
    Built-in IO ports on one side
    CPU oriented so it can be cooled by the power supply fan
    CPU and RAM perpendicular to expansion slots
    Additional space for extra cooling
    Micro ATX (9.6 "x9.6")
      Smaller machines
NLX
  Standing expansion.
BTX
  Should provide better cooling options than ATX
  Three different sizes:
    Full (326 x 266 mm)
    microBTX (264 x 266 mm)
    picoBTX (203 x 266 mm)
ATX
BTX
NLX
Notes: If you’re overwhelmed by all the features and details above, you’ll be relieved to hear that, when it comes to motherboard size, your options are pretty simple. The vast majority of today’s consumer motherboards come in one of three sizes: ATX, Micro-ATX, and Mini-ITX.

## Slide 12: Integrated and Non-Integrated
Many motherboards are integrated and come with CPU, video card including GPU, network card, bus controllers and everything ready built into the card itself.
  Typically for e.g. cheap laptops etc..
Non-integrated motherboards.
  Fits additions as expansion cards
  Disk controllers, video cards, network cards,…
Increasingly unclear distinction nowadays…

## Slide 13: Power supply
Transforms 220 V, 50 Hz AC (AC) to the voltages DC (DC) components of the motherboard need
  3,3 V
  +/-5 V
  +/- 12V
The type of power supply you can use depends on the other things, form factor on the motherboard
Notes: https://www.fsp-group.com/en/knowledge-tec-26.html#:~:text=In%20a%20nutshell%2C%20an%20AC,DC%20electricity%20supply%20to%20operate.

## Slide 14: CPU

## Slide 15: CPU Socket
The CPU is connected to the motherboard through a socket (or in an expansion slot)
Different types with different number of slots for CPU pins
Speed on Front Side Bus (FSB)
Depends on the motherboard
1980
1994
2004
2011

## Slide 16: CPU cooling
CPU
  Power (W = J / s) is energy per unit time, 1 Watts = 1 Joules per second
  manifests itself as heat generation
  E = UI, U = RI (Ohm's law), E = RI2
  => The heat rises with the square of the current
Air cooling
  Uses fan
Liquid cooling
  Pumps away the heat with liquid
  Typical water (or liquid nitrogen)
Ohm's law can be expressed as I = U / R where
I = current (ampere, A), U = electrical potential (volts, V),R = resistance (ohms, Ω)
Electrical Power = energy
E=UI=RI2
Notes: https://www.engineeringtoolbox.com/ohms-law-d_1658.html

## Slide 17: Troubleshooting: CPU
Typical problems are cooling or electricity
Symptoms
  PC does not boot or load OS
  PC crashes with some applications
  Sudden POST errors for a lot of different equipment
  Heat problems (typical)
  PC boots, but stops / freezes / reboots after a few minutes
  Mt
  itigation: better cooling
error message displayed on the monitor during the power-on self test if the BIOS encounters some kind of problem while starting the PC.

## Slide 18: RAM

## Slide 19: Bit, Byte and Word
BIT
  Binary DigIT
  On/off
  1 or 0
BYTE
  8 BIT
  Can store e.g. an alphanumeric character
  Smallest addressable device in RAM.
WORD
  In computer architecture, this has several meanings
  The size of a register
  The number of BIT the CPU can process as a unit
  Addressing unit
Notes: BYTE, WORD (16), DWORD (32) and QWORD (64) are MicrosoftSpeak - not everyone uses these terms

## Slide 20: Types of Memory Problems
Configuration
  More memory than PC or OS support
  BIOS CMOS error
Hardware
  Defective pieces or modules
  Incompatible modules.
Installation
  the module is not inserted correctly into the slot
  Tracks ("socket" defective, or should be cleaned)

## Slide 21: Memory troubleshooting
Other components can cause problems that look like memory problems!
Memory problems typically show up:
  First booting
  Immediately after installing
  new RAM module
  new software or new OS
  After new hardware has been added, or old removed
  Completely without any obvious cause
  Corrosion ("rust")
  Heat damage

## Slide 22: Common RAM issues
PC does not boot, POST beep code
  Memory inserted, or configured, incorrectly
PC boot to blank screen
  Memory module detached
  Memory module of the wrong type
POST memory count error
  Incorrect RAM module type
"Memory Error" message
  Compatibility issues with old and newly installed RAM
  RAM module about to break

## Slide 23: Peripheral buses & equipment

## Slide 24: I/O devices
Almost endless selection of I / O
Common concepts
  Gate
  Bus (daisy chain or shared direct access)
  Controller (host adapter)
I/O instructions control devices
The collaboration with the OS usually takes place through a driver that translates the OS instructions into Controller instructions
A host adapter, HBA (host bus adapter), or host controller
allowing communication with devices
  some host adapter can be added to a computer, like a PCI card, others are integrated into the computer motherboard (e.g., hard drive host adapter).
  Integrated host adapter are commonly referred to as IDE ports or SATA ports on a motherboard.

## Slide 25: Addressing devices: Direct, Memory-mapped
Memory-mapped I/O uses the same address space to address both memory and I/O devices.
The CPU instructions used to access the memory can also be used for accessing devices.
Port-mapped I/O often uses a special class of CPU instructions designed specifically for performing I/O, such as the in and out instructions found on microprocessors based on the x86 and x86-64 architectures
Memory-mapped I/O (MMIO) and port-mapped I/O (PMIO) are two complementary methods of performing input/output (I/O) between the central processing unit (CPU) and peripheral devices
Resource conflicts can arise when two different subjects try to use the same Object (resource)

## Slide 26: Expansion buses
Let us add new functionality in the form of cards and peripherals
Connected to slots on the motherboard where we mount the expansion card
Different technologies
PCI, AGP, ISA, PCIe
Perform communication between the card controller and the chipset
Expansion card

## Slide 27: Old expansion cards and slots

## Slide 28: PCI
32 and 64 bit data
Bit rate up to 66 MHz, 533 MB / s (64 bit)
CPU independent
Backcompatible with ISA, EISA
Plug and Play (PnP) support

## Slide 29: Accelerated Graphics Port (AGP)
Made to support 3D graphics
Connected directly to Northbridge
32 bit, 66 MHz
Bit rate from 266 MBps to 2133 MBps depending on version
Versions 2X, 4X, 8X transmitted data 2x, 4x and 8x per clock cycle

## Slide 30: Data Storage (Hard disk)

## Slide 31: Data Storage
Used for permanent storage of large amounts of data
  Punched card
  Punch tape
  Diskette, Flash Mem
  Zip, Jazz
  Disk
  CD, DVD
  Magnetic tape (reel tape, cassette)
  Transfer to the processor via a controller
  Use different HBA: IDE / EIDE, SATA, Small Computer System Interface (SCSI),…

## Slide 32: Paper as a storage medium

## Slide 33: Files, Organization of data
Data is basically a collection of 0s and 1s which in their context represent a document, image, music etc.
This collection is called a file
A file has a name that makes it easy to identify
In an identification field that is added to the file, in addition to the name, there is also information such as the size of the file, when it was created, the owner of the file, ...............

## Slide 34: Disk

## Slide 35: Disks
Disks ...
  Provides lasting storage
  is cheaper per byte than RAM (currently)
  has greater capacity.
  are many orders of magnitude slower.
Important parameters are
  storage space
  I/O bandwidth
Because...
  ... there is a colossal speed difference (ms vs ns ~ 106) with RAM.
  ... disk I/O is very often the most important performance bottleneck.
the speed with which the data transfer takes place between the hard disk drive and RAM

## Slide 36: CD/DVD/Blue-Ray (1)
A CD can store 700 MB, DVD 4 GB on each side, Blue-Ray 25GB per layer (up to 8 layers in RW)
https://www.youtube.com/watch?v=H-jxTzFrnpg

## Slide 37: CD/DVD/Blue-Ray (2)
https://www.youtube.com/watch?v=H-jxTzFrnpg
https://www.youtube.com/watch?v=2lzKy8d9BKE

## Slide 38: Backup
All types of storage media can break
Important data should therefore be stored in more than one place
It's too late to think about backing up after a crash
Home burning has become more popular lately!
Remember the legal / ethical side of data copying !!

## Slide 39: RAID (Some types)
Designation | Technique |  | 
RAID 0 | Striping | Faster access | 
RAID 1 | Mirroring | Faster access, more reliability | 
RAID 5 | Striping and distributed parity blocks | Faster access and more reliability | 

## Slide 40: Protection against errors and crashes (RAID)
Large disk banks can leave each disk on its own two feet, RAID0
  or generate continuous copy of all disks, RAID1
  or use other securing techniques (e.g. striping)
RAID5 creates a checksum (XOR) for two disks and stores this on a third disk. This is good enough if a disk crashes.

## Slide 41: Typical Hard Disk Problems
common causes
  Fault in controller / adapter
  Incorrect pairing of adapter and disk
  Errors on the disks themselves
  CMOS config error
  Resource conflict
  Corrupt or missing Boot partition
  Virus in boot partition
  Defective (mechanical defects)
A boot partition is a volume of the memory that contains the system files used to start the operating system.

## Slide 42: Typical error messages (accordingly)
Hard disk configuration error
  Incorrect CMOS config parameters
  Loose data cable
Hard disk 0 failure
  Incorrect CMOS config
  Poor connection to power supply.
Hard disk controller failure
  Poor cable connection
  Poor connection to power supply

## Slide 43: USB and Flash memory

## Slide 44: USB – Universal Serial Bus
Supports up to 127 different connected devices
  Expands with hub
High speed data transfer.
  USB 1.1: 12 Mbps (max)
  USB 2.0: 480 Mbps (max)
  USB 3.0: 5 Gbps (max)
Variable bitrate
  Low speed channel for slow equipment
Four main types of data transfer.
  Bulk, interrupt, isochronous, control.
PnP and hotpluggbar.
Can be used for charging

## Slide 45: Flash Memory
Two types: "NOR" and "NAND”
NOR (parallel-connected)
  Random Access reading / writing
  Best for programs
  Widely used in mobile phones.
NAND (serial-connected)
  Read in blocks (as HD)
  Cheaper, more transistors on smaller area
  Faster to read from than to write to
  Best for data.
You can (on both types) only delete blocks!
Holds to about 100,000 write / delete
512MB -> 256 GB (2009) -> 1 TB
NOR vs. NAND Flash Memory
https://www.youtube.com/watch?v=jAQiMWmSlIo

## Slide 46: Peripherals

## Slide 47: Keyboard
Typically, 104-key IBM PC is standard (qwerty)

## Slide 48: Mouse (optical)
LED or LED laser emits a beam of light
Low resolution «camera» (20x20 px ->) takes «pictures» about every 1/10 second (often more often)
Chip measures / calculates the difference between images and calculates position change

## Slide 49: Screen
Two main types
Cathode ray tubes (CRT – Cathode Ray Tube)
  Was usually long, almost gone …
Flat-panel
  LCD – Liquid Crystal Display
  Plasma display, FED, LED, polymer display, OLED
https://www.youtube.com/watch?v=K-kxIP3FhCk
https://www.youtube.com/watch?v=qOsibeDX8jM

## Slide 50: What should we know?

## Slide 51: What should we be able to do now?
What motherboards and chipsets are
CPU (vs GPU) and why cooling is necessary
RAM: types and roles
Hard disk, addressing, partitioning, parity and RAID
Peripheral equipment, expansion and peripheral buses
The principle behind LCD monitors

## Slide 52: Next lecture
Operating system
  What is it really for?
  How does it relate to everything we've been through so far
  What is the difference between the different (Windows, Linux, OSX)
  How to work in a shell

## Slide 53: For optional self-study
For those who want to learn some topics more in depth to better understand, here are some extra topics related to today's teaching, it must be expected some personal work to understand these topics.
There will be no questions on the exam from these, and this is therefore not considered to be part of the syllabus.

## Slide 54: SSD: Solid State Drive
(Most often) the same storage technology as Memory Stick (NAND)
50-100 times faster (shorter access time) than HardDisk
  No mechanics, arms that have to be moved, etc.
Limited life, just like Flash Memory.
10-20 times as expensive per GB.
Available up to 4TB (?).

## Slide 55: Motherboard about 2011
Kilde: http://goo.gl/ybDrs
Notes: ASUS Crosshair V Formula AM3+ AMD 990FX SATA 6Gb/s USB 3.0 ATX AMD Gaming Motherboard

## Slide 56: Screen
An image element (pixel) consists of 3 colors (red, green and blue)
All items on the screen were updated several times per second.
The size of the screen is stated as the length of the diagonal.
Controlled by graphics card with memory.

## Slide 57: Screen

## Slide 58: Video-card
Interprets and controls what is to appear on the screen
Own memory, determines the maximum resolution and color depth
Dot pitch; the distance between two pixels(0,25 mm)

## Slide 59: Graphics
There are many standards for on-screen graphics.
Mostly, the standards evolve after the development of screen technology.
Example: SVGA (Super Video Graphics Array)
  Resolution : 800*600  1600*1200 pixler
  Color depth : 256( 8 bit)  ca. 16 millioner (24 bit)
  Refreshment rate : 50  100 Hz
The number of possible simultaneous colors depends on the size of the video memory.

## Slide 60: «Countless »standards (px, colors)

## Slide 61: Flat panel (LCD)
Each pixel has an address
Only changed pixels are updated
Very stable image of good quality
Problematic in sunlight

## Slide 62: Example: An LCD subpixel
Light from background board
Polarizing filter (vertical)
Liquid crystal that "twists" the polarization when you "turn on power"
Polarizing filter (horizontal)
Colour

## Slide 63: So far
Generally
  Digital vs analog, def computer
Data types
  Tall, text, images, sound
CPU
  Structure
  Register
  Instructions

## Slide 64: Addressing binary
With 7 binary digits (bits), 27 = 127 + 1 = 128 = «house» can be addressed.
At each address "lives" a byte.
0000001
0000011
0000101
0000111
1111111
0000000
0000010
0000100
0000110
1111110
Binærgaten

## Slide 65: System resources
The buses use one or more types of system resources
  I / O port addresses
  IRQ= Interrupt Request
  DMA channels=Direct Memory Access (DMA)
Resource conflicts can arise when two different subjects try to use the same Object (resource)
Plug-and-Play (PnP): Configuration standard that automatically allocates system resources to expansion cards and equipment

## Slide 66: Magnetic storage / reading
Storage
  When the electromagnet is supplied with power, the surface under the magnet is magnetized.
Reading
  When the surface under the magnet is magnetized and passes the magnet, power will be generated (induced).
Magnetized area = 1
Not magnetized = 0

## Slide 67: Magnetic tape

## Slide 68: RAM for PC
Addresses
  16 bit = 65536 = 64 KiB
  20 bit = 1MiB
  32 bit = 4 GiB
  64 bit = 16 EiB
DRAM - Dynamic RAM
  Must be refreshed; read / rewrite.
SDRAM - Synchronous DRAM
  In step with the CPU.
SRAM - Static RAM
  Does NOT need to be refreshed, faster a DRAM, but more expensive to produce and needs more transistors per bit stored

## Slide 69: Physical organization
DIP (Dual In-line Pin) right on the motherboard.
SIMM (Single In-line Memory Module)
  Snapped on the motherboard
  DRAM; 60 to 120 ns
  SRAM and cache; 20 ns
  Odd Parity
    10010110 1
    Used to check if errors have occurred.
DIMM (Dual In-line Memory Module)
  Contact points on both sides
  64 bit bus connection.
    168, 184, eller 240 bus connections.
  RDRAM is a variant
    There are many variants in terms of number of connection points, type of bus etc.

## Slide 70: DRAM form factors (some)

## Slide 71: DRAM technologies
Previously
  Asynchronously, the system clock did not follow
  FPM, EDO, etc..
Current
  Single Data Rate RAM
    One read / write per clock / bus pulse
  Double Data Rate RAM (DDR, DDR2, DDR3)
  RAMBUS
RAM performance depends more on the package and bus, than on the RAM itself.

## Slide 72: DRAM characteristics
CAS (Column Adress Strobe) latency
  Number of clock cycles it takes to move requested data to the legs of the RAM module
  For example. CL2 (two clock cycles)
Dual or quad channel
  Motherboard-dependent - number of parallel RAM channels.
Single vs double row
  Double-ranked has two separate groups of RAM chips that are accessed separately by the RAM controller.

## Slide 73: Win7: devmgmt.msc
In win7 / 8/10 you can inspect which resources in MMC snapin devmgmt.msc

## Slide 74: Data buses

## Slide 75: Motherboard: Buses
Serial vs parallel
Data / Address / Control / Power
Width (#bit), tempo (Hz)
Two main buses:
System / FSB
connects CPU to Northbridge / RAM
Expansion
Connects the chip to expansion slots

## Slide 76: Chipset
The controllers that control the exchange of data / instructions / interrupt signals between the CPU and other equipment are often referred to as the motherboard chipset
In the last ten years, these have typically been two main controllers
  Northbridge (Intel: Memory Controller Hub)
    CPU and memory (RAM)
    High speed equipment: graphics card
    Communication with Southbridge.
  Southbridge (Intel: IOController Hub)
    Peripherals (typically outside the cabinet)
    Minor controls
    Secondary and old-fashioned buses

## Slide 77: The transport system
"Cables" with parallel and serial "wires"
Width * Speed = Bandwidth

## Slide 78: The tasks of the buses
Addressing of data
Shipping of data
Synchronization of machine components
Flow control between the components
Signaling between the components
Power supply for some components

## Slide 79: Addressing
Width from 20 to 64 bits
  32 bit allows to address (232=) 4 GB
There are techniques of sending multiple bits / bytes at a time.
  Needs less width on the bus
  Needs more control in the components

## Slide 80: Synchronization
Internally in the machine there will be several clocks
CMOS (BIOS) has a "regular" (real-time) clock
All other clocks are actually clockmakers.
Synchronous components
  Keeps the same or similar pace
Asynchronous components
  Each keeps his own pace

## Slide 81: Interrupt signals
Interruption signal is a message that something has happened.
  It's the mechanism that lets the CPU and controllers know that something / someone wants something done.
IRQ - Interrupt Request
Such signals can be given different priority
Own components for registration and further processing

## Slide 82: Interrupt (and Exception) Handling
The IA-32 architecture has an IDT with pointers to 256 different interrupts and exceptions
32 (0 - 31) predefined and reserved
224 (32 - 255) user / OS defined.
Each interrupt has a pointer in the Interrupt table (IDT) and a unique index value that provides handling as follows:
  Process runs when the interrupt occurs
  Save state, context switch and find the correct interrupt handler
  Execute interrupt trades
  Recover (interrupted) process
  Continue execution
user
kernel
IDT:
disk interrupt (x)
Interrupt routines:

## Slide 83: Storage development (1)

## Slide 84: Storage capacity (2)

## Slide 85: Density and price (3)

## Slide 86: The structure of the disk
All arms move at the same time
Each arm has 2 heads
In / out 50 times / sec
Spin: 3600-7200 (15000) RPM
Search time: 10-20 ms
Data rate: 5-40 MB / sec ~ 300Mbps w / SATA)

## Slide 87: Reading heads
The reading heads float on the air above the plate (0.001 mm)

## Slide 88: Disk organization
Track
  The area the reading head covers on a rotation.
Sector
  The smallest part of a track that can be read
Cylinder
  All tracks in the same position on the disc
512 bytes per sector * 51 sectors per track * 723 cylinders * 14 read heads = 264305664 B = 252 MB

## Slide 89: Disk Access Time
+ Rotation delay
+ Transfer time
Search time
Disk access time =
+ Other delays
Disk plate
Disk arm
Disk head
block X
in memory
Will have
block X

## Slide 90: H-Disk addressing of sectors
Previously (and due to backward compatibility) CHS (Cylinder, Head, Sector) or Extended CHS was used.
  Originally limited to 1024 C, 16 H, 63 S = 528 MB
  BIOS Interrupt 0x13 extended to 8G at 0-254 Head
  24 bit address, 512 B sector = 8G hard drive
Now used LBA (Logical Block Adressing)
  Originally for SCSI, then for ATA / SATA
  The sectors have logical linear LBA addresses 0,1,2,3…
  C 0, H 0, S1 = LBA 0, …
  32 bit addresses give max size 2TB
  LBA is supported by all modern OS and BIOS
In the future, GUID seems to take over
  Supported by UEFI
  64 bit addresses
  allows in principle disks up to 8 ZiB (assuming 512 Byte blocks)

## Slide 91: The logical organization of the disk (hierarchy)
Cluster
  Minimum unit read by the operating system, minimum 1 sector.
File
  Minimum device referenced by the operating system, minimum 1 cluster.
Catalog
  File for organizing files
Partition.
  Organization of directories; e.g. C :

## Slide 92: Low-level formatting
Low level formatting is done by the manufacturer
Addresses are written on each sector
The disk is initialized with zero values
Defective areas are marked
The interleave pattern is set
The example shows 3: 1 interleave

## Slide 93: Partitioning
Partitioning is done by supplier (or user)
Made from «DOS» with the program FDISK
Creates MBR (Master Boot Record) at the start of the disk
Used by the BIOS to boot the operating system
Minimum 1 partition (primary)
Can add secondary (extended) partitions
Cannot have two operating systems in the same partition (other than as Virtual Machine)

## Slide 94: High-level formatting
High-level formatting is done by the supplier (or user)
Can be done from DOS with the program FORMAT
Receives warning from operating system if it is primary partition
Adds content from MBR into the startup sector
Not all disks can be booted
Stock root directory
Defines how many sectors there are in a cluster
Builds file allocation tables (FAT)
FAT12, FAT16, FAT32, (NTFS, Ext3)

## Slide 95: Fragmentation
Fil#1
Fil#2
Fil#3
Start
Fil#1
Edit
Fil#1
Fil#3
Defrag
Delete
Fil#1
Fil#3
Fil#1

## Slide 96: Parity bit
In order to be able to identify "bad blocks" (sectors with errors), each sector has a parity byte that is used to check whether errors have occurred.
Parity check was part of 7bit ASCII:

## Slide 97: Parity bit
1 parity bit can only detect odd number errors!
Uses CRC checksums that provide the opportunity to detect far more errors (more in the penultimate lecture)
Parity can be easily generated with XOR!
Using smart coding, you can create better checksums. (cf. social security number)
parity?

## Slide 98: Error Correcting Codes (ECC)
Based on the Hamming distance between the codes
Example
In this code set, there is always at least three bits difference between all the codes The hammering distance between A and B is 4, B and C 3, etc.

## Slide 99: ECC (2)
Reading 010100, which letter should it (probably) have been?
  The one with the least Hamming distance in the code set.
With Hamming-distance 3 in the code set, you can detect up to two error codings (bit-flips) and correct one.
With Hamming distance 5 in the code set, you will be able to detect up to four errors per pattern and correct two

## Slide 100: Buses / sections: ATA, SATA
(Parallell) ATA
  (Parallel) ATA
  Versions 1-7
  Original IDE
  Supported LBA and DMA
  Cable with 80 parallel conductors
  Max 133 MBps.
  SATA: Serial
  Latest version supports up to 6 Gbps (v. 3.0)
  Cables up to 8 m
  eSATA for external connection
  HotPlug!

## Slide 101: SCSI
Allows series connection of equipment.
  Each must have their own ID.
Most used on servers
Versions 1-3
A collection of different standards!
iSCSI is e.g. a combination of Etrhernet and SCSI

## Slide 102: Device controllers
I / O devices often consist of
  Mechanical component ("the device itself")
  Electronic component
The electronic component is the device controller.
  "A small microprocessor"
  Can possibly handle several units
The tasks of the controller
  Receive instructions
  View status
  Convert serial bitstream to block of bytes
  Perform error correction as needed
  Make data available in primary memory (RAM)

## Slide 103: I / O ports and addresses
Each controller has some registers that are used to store status and communicate with the CPU
  Can write to these to control the device
  Can read others to find the condition of the device.
May also have data buffer
  Video RAM on video card
  Cache ON disk
Can write registers / buffer using I / O ports
Can also use the memory mapped I / O

## Slide 104: Ex: read from disk
Pentium 4
Processor
registers
cache(s)
I/O
controller
hub
memory
controller
hub
RDRAM
RDRAM
RDRAM
RDRAM
PCI slots
PCI slots
PCI slots
system bus
(64-bit, 400/533 MHz ~24-32 Gbps)
hub interface
(four 8-bit, 66 MHz  2 Gbps)
PCI bus
(32-bit, 33 MHz  1 Gbps)
RAM interface
(two 64-bit, 200 MHz  ~24 Gbps)
disk
file system
application
disk

## Slide 105: PCIe
High speed serial bus architecture
Supports multiple channels
Different tracks avh channel number
Structure
Point-to-point
Packet-based and routed a la network
Addresses and data are in the same package
High bit rate
Each channel supports duplex, 2.5 Gbps each way
SUPPORT FOR SEVERAL GRAPHIC CARDS
Why single direction?

## Slide 106: Start-up

## Slide 107: BIOS – BASIC I/O SYSTEM
Software for controlling essential components
  For example. Keyboard, screen, disks, serial ports, …
Stored on ROM chip
Three main functions
  Boot PCs
  Test and verify hardware
  Provide interfaces between hardware and software.

## Slide 108: Boot -the sequence
.The power supply starts up
The primary part of the BIOS is loaded into RAM
  The CPU reads the start address of the BIOS boot program.
Boot type confirmed.
  Cold boot: turns on
  Warm boot: restart / rest, does not run POST
  When PC restarted or reset, does not run POST.
Power On Self Test (POST) begins.
  Error messages are given as "beep codes"
Video adapter software loads.
The BIOS for other equipment is loaded
  BIOS startup screen loads
  Error messages are displayed as text..
CMOS configuration tested.
  Checks that equipment listed in CMOS is present and working.
Ports assigned and equipment configured.
Hardware configuration confirmed
BIOS displays summary screen
Operating system located and loaded (MBR).
Boot fails:
  When the PC fails to complete the BIOS and load the OS
  Typical causes are loose or missing components, and / or OS / driver errors on disk.

## Slide 109: Power On Self Test (POST)
Error codes are (mainly) dependent on the BIOS manufacturer
Two types:
  Beep codes
    Long and short tones in speaker
  Error messages
    To screen
    1xx Motherboard, 2xx RAM, 3xx Keyboard, 17xx HD,…
    3-4 digits with some explanation
    «BIOS ROM checksum Error: System halted»
    Hard disk install failure »
    Memory Test Fail.
  Easy BEEP in speaker when POST performed
109

## Slide 110: CMOS
BIOS setup program: Used to configure settings stored in CMOS.
CMOS settings ≈ Hardware configuration
SETUP:
  Typically has menus to set:
  Default Settings
  Boot medium order
  System date and time
  Hard disk, floppy, ..
  Video display
  Advanced settings: Motherboard, CPU, chipset
  Plug and Play (PnP) options, power management, security and passwords, integrated controllers for peripherals.

## Slide 111: BIOS update
The BIOS "determines" what kind of equipment the PC may have connected
Upgrading ("flashing") of the BIOS is occasionally needed to solve special problems
You can corrupt the BIOS chip by interrupting during updating, or trying to enter the wrong BIOS
Now replaced by different types of firmware
111

## Slide 112: BIOS->UEFI
BIOS is for 16 bit machines…
Supports only 1 MiB of memory.
Is in the process of being replaced with Unified Extensible Firmware Interface (UEFI)
  Supports both 32 and 64 bit instructions from startup
  Supports a minimum of 2GB of memory
  Supports a new addressing method for partitions and blocks on the Hard Disk (GPT instead of MBR) which allows hard disks larger than 2 TB to be used -> 8 * 2 ^ 70
112