## Slide 2: Digital technology
TK1104-1 22H
Lecturer: Toktam Ramezanifarkhani
Toktam.Ramezanifarkhani@kristiania.no
Toktamr@ifi.uio.no
Elsa Lossius
ello008@student.kristiania.no

## Slide 3
Instruction programming Computer Organization

## Slide 4: CPU Programming Computer Organization

## Slide 5: Computer Organization
All computers perform IPOS
  Input, Processing, Output, Storage
Here, we concentrate on how IPOS is carried out through the fetch-execute cycle
This requires that we study
  the structure of the components in the computer
  the function of those components
    how the CPU works
    the role of memory
    the role of I/O devices
Notes: Demonstration of the fetch execute cycle
The Fetch Execute Cycle

## Slide 7: The Components of the CPU
Control Unit
  Operates the fetch-execute cycle
  Decodes instructions
  Sends out control signals
Registers
  Data register(s)
  Control unit registers
Arithmetic-Logic Unit
  Contains circuits to perform arithmetic and logic operations
    adder/subtracter
    negater (convert + to -, - to +)
    multiplier
    divider
    shifter
    rotate
    comparator
  Sets status flags

## Slide 8: The Structure of the Computer

## Slide 9: The Bus
Address bus:
  CPU sends address to memory or I/O subsystem
  Address is the location of the item being moved
Control bus:
  CPU sends out commands to other devices
    read, write for memory
    input, output, are you available for I/O devices
  Devices send signals back to the CPU such as interrupt
Data bus:
  Used to send data and program instructions
    from memory to the CPU
    from the CPU to memory
    between I/O device and the CPU
    between I/O device and memory
  Size of data bus is often size of computer’s word

## Slide 10: Registers
Temporary storage in the CPU
  Store values used during the fetch execute cycle
  PC – program counter
    Memory location of next instruction, used during instruction fetch
  Data registers
    To store temporary results during execution
    Some computers have one, the accumulator (AC), others have several, maybe dozens (eax, ebx, ecx, edx or R0, R1, R2, …, R31)
  IR – instruction register
  Current instruction, used during decoding
Status flags
  To store information about the result of the previous ALU operation
    positive, negative, zero, even or odd parity, carry, overflow, interrupt
EBX is a "base" register
EAX is an "accumulator"

## Slide 11
CPU performs the fetch-execute cycle
  Fetch next instruction from memory
  Decode the instruction
  Execute the instruction
  Store the result
To execute a program

## Slide 12: Fetch-Execute Cycle
CPU needs to know What to do.
CPU needs:
Where is the instruction
What is the instruction

## Slide 13: Processor operation with a program
High level language
  • C #, JAVA (and many others)
  • Interpreted in an environment
  (eg a virtual machine)
Low level language
  • C, C ++ (and more)
  • Compiled to Assembly and then
  machine instructions
Machine language (IA32, IA64, etc.)
  • Assembler language
  (each command corresponds to a
  machine instruction: mov eax, [00AF3B13])
Instructions for the processor = programs
  • Retrieved to the processor from memory (RAM)
void main( ) // start of the program
{ int a, b, c; // use 3 integer variables
scanf(“%d”, &a); // input a
scanf(“%d”, &b); // input b
if(a < b) // compare a to b, if a is less then b
c=a + b; // then set c to be their sum
else c=a - b; // otherwise set c to be their difference
printf(“%d”, c); // output the result, c }

## Slide 14: Example: A Program
We use the following C program to better understand the fetch-execute cycle
#include <stdio.h> // input/output library
void main( ) // start of the program
{
int a, b, c; // use 3 integer variables
scanf(“%d”, &a); // input a
scanf(“%d”, &b); // input b
if(a < b) // compare a to b, if a is less then b
c=a + b; // then set c to be their sum
else c=a - b; // otherwise set c to be their difference
printf(“%d”, c); // output the result, c
}

## Slide 15: Program in Assembly Language
Input 33 // assume 33 is the keyboard, input a value from keyboard
Store a // and store the value in the variable a
Input 33 // repeat for b
Store b
Load a // move a from memory to CPU, a location called the accumulator
Subt b // subtract b from the accumulator (accumulator = a – b)
Jge else // if the result is greater than or equal to 0, go to location “else”
Load a // otherwise, here we do the then clause, load a into accumulator
Add b // add b (accumulator is now a + b)
Store c // store the result (a + b) in c
Jump next // go to the location called next
else: Load a // here is the else clause, load a into the accumulator
Subt b // subtract b (accumulator is now a – b)
Store c // store the result (a – b) into c
next: Load c // load c into the accumulator
Output 2049 // send the accumulator value to the output device 2049, assume
// this is the monitor
Halt // end the program
void main( )
{ int a, b, c;
scanf(“%d”, &a);
scanf(“%d”, &b);
if(a < b)
c=a + b;
else c=a - b;
printf(“%d”, c);
}

## Slide 16: Program in Assembly Language
Input 33 // assume 33 is the keyboard, input a value from keyboard
Store a // and store the value in the variable a
Input 33 // repeat the input for b
Store b
Load a // move a from memory to CPU, a location called the accumulator
Subt b // subtract b from the accumulator (accumulator = a – b)
Jge else // if the result is greater than or equal to 0, go to location “else”
Load a // otherwise, here we do the then clause, load a into accumulator
Add b // add b (accumulator is now a + b)
Store c // store the result (a + b) in c
Jump next // go to the location called next
else: Load a // here is the else clause, load a into the accumulator
Subt b // subtract b (accumulator is now a – b)
Store c // store the result (a – b) into c
next: Load c // load c into the accumulator
Output 2049 // send the accumulator value to the output device 2049, assume
// this is the monitor
Halt // end the program

## Slide 17: Program in Machine Language
Assembly code version of our C program is stored in the computer in machine language
  The first four instructions might look like this:
1000100 0000000000000000000100001 – input (from keyboard)
1000111 0010011000100101101010001 – store the datum in a
1000100 0000000000000000000100001 – input (from keyboard)
1000111 0010011000100101101010010 – store the datum in b
op code operand (datum)

## Slide 18: Fetch-Execute Cycle – (reminder)
CPU needs to know What to do.
CPU needs:
Where is the instruction
What is the instruction
When memory sends an instruction to CPU, it uses data bus
When CPU sends the instruction to the memory, control bus is used

## Slide 19: Fetch-Execute Cycle: Details
Fetch:
  PC stores address of next instruction
  Fetch instruction at PC location
  Increment PC
  Instruction sent over data bus
  Store instruction in IR
Decode:
  Decode opcode portion in IR
  Determine operand(s) from instruction in IR
Execute:
  Issue command(s) to proper circuits
  Use data register(s)
Store result
  In AC (or data register), or memory
Input 33
Store a
Input 33
Store b
Load a
Subt b
Jge else
Load a
Add b
Store c
Jump next
else: Load a
Subt b
Store c
next: Load c
Output 2049
Halt

## Slide 20: Fetch-Execute Cycle: Example
Assume our program starts at location 5,000,000
  PC: 5,000,000
  IR: -------
Fetch instruction
  PC: 5,000,000
  IR: 1000100 0000000000000000000100001
  Increment PC to 5,000,001
Decode instruction
  Input operation (obtain input from keyboard)
Execute:
  Take input value from keyboard
  Move to AC
 | Input 33 | Store a | 
The address of the starting block of the program in the memory is 5,000,000

## Slide 21: Continued
Fetch instruction
  PC: 5,000,001
  IR: 1000111 0010011000100101101010001
  Increment PC to 5,000,002
Decode instruction
  Store datum to memory location 0010011000100101101010001 (memory location storing variable a)
Execute:
  Move datum from AC over data bus to memory location a
    NOTE: the next two instructions are almost identical except that the second input’s datum (from the third instruction) is sent to memory location b instead of a)

## Slide 22: Continued
Load a
  Fetch instruction at 5,000,004
  Increment PC to 5,000,005
  Decode – load instruction, operand is a from memory
  Execute – loads datum at location a into AC
Subt b
  Fetch instruction at 5,000,005
  Increment PC to 5,000,006
  Decode – subtract instruction, operands are AC register and b from memory
  Execute – fetch b from memory, send AC and b to subtracter circuit
  Store result in AC
  Set status flags as appropriate (negative, positive, zero, carry, overflow)
Input 33
Store a
Input 33
Store b
Load a
Subt b
Jge else
Load a
Add b
Store c
Jump next
else: Load a
Subt b
Store c
next: Load c
Output 2049
Halt

## Slide 23: Continued
Jge else –a branch instruction
  Fetch instruction at 5,000,006
  Increment PC to 5,000,007
  Decode instruction
  Execute instruction – if positive or zero flag are set (1) reset PC to 5,000,011 (branches to “else”) otherwise, end instruction
Next instruction fetch is 5,000,007 or 5,000,011
Next few instructions executed depend on the previous conditional branch
  Either “Load a”, “Add b”, “Store c”, “Jump next”
  Or “Load a”, “Subt b”, “Store c”
Jump next – PC altered to 5,000,014 (location of “next”)
Output 2049 – outputs value in AC to device 2049 (the monitor)
Halt – ends the program
Input 33
Store a
Input 33
Store b
Load a
Subt b
Jge else
Load a
Add b
Store c
Jump next
else: Load a
Subt b
Store c
next: Load c
Output 2049
Halt

## Slide 24: Execute Memory Read instruction after Decode:
write
Execute Memory Write instruction after Decode:

## Slide 25: Tutorials
Demonstration of the fetch execute cycle
Memory read operation
Memory write operation
https://www.youtube.com/watch?v=xs5oq-i_rTc&t=65s
Fetch Decode Execute Cycle in more detail
https://youtu.be/jFDMZpkUWCw

## Slide 26: CPU Performance

## Slide 27: Microcode and System Clock
Each clock cycle, the control unit issues instructions to the devices in the computer (1 part of the fetch-execute cycle, not a full instruction)
These instructions are in the form of microcode
  1 bit per line on the control bus
Example: instruction fetch
  Move PC to address bus, Signal memory read, might look like
    10000000000000100000000000000000000000000000000000
  1 clock cycle = 1 microinstruction executed
Fetch-execute cycle might have between 5 and 30 steps depending on architecture
Clock speeds are given in GHz
  1 GHz = 1 billion clock cycles per second, or 1 clock cycle executes in 1 billionth of a second (1 nanosecond)

## Slide 28: Measuring CPU Performance
A faster clock does not necessarily mean a faster CPU
Other impacts of CPU performance include
  Word size – size of datum being moved/processed
  Cache performance (amount and usage of cache)
  The program being run (some programs are slower than others)
  How is the OS load
  Virtual memory performance
  Any parallel processing hardware?
Best measure of CPU performance is to examine benchmark results
  CPU1 2.5 GHz, 12 stage fetch-execute cycle requiring 20 cycles to complete 1 instruction
  CPU2 1 GHz, 5 stage fetch-execute cycle requiring 8 cycles to complete 1 instruction
  CPU1 = 20 / 2.5 GHz = 8 nanoseconds / instruction
  CPU2 = 8 / 1 GHz = 8 nanoseconds / instruction

## Slide 29: Memory

## Slide 30: Role of Memory
Memory is referenced at every instruction
  1 instruction fetch
  Possibly 1 or more data accesses
    data read as in Subt b
    data write as in Store a
  In Intel x86 architecture, Add x, 5 involves 3 memory references
    instruction fetch
    load x for addition
    store result in x
Random Access Memory: Dynamic and Static
  There are several types of RAM
  DRAM – “main memory”
    made of capacitors
    requires timely refreshing
    slow but very cheap
  SRAM – cache and registers
    much faster-made of flip fops
    but more expensive
  ROM – read only memory
    used to store boot program, BIOS
    information permanent (cannot be altered)
    even more expensive
Notes: Dynamic Random Access Memory (DRAM).

## Slide 31: Memory
https://www.mphysicstutorial.com/2020/12/semiconductor-memory-types-ram-rom-dram.html
https://m.facebook.com/Tipsoncomputermaintenanceandknowledge11/posts/ram-random-access-memory-and-rom-read-only-memory-are-the-two-important-memory-t/391442481220798/
RAM (random access memory)
cannot hold the data without the power, whereas
ROM (read-only memory)
can hold the data even without the power
With RAM, writing data is a much faster and lightening process, whereas ROM, writing data speed is much slower as compared to RAM.
RAM and ROM: both are random access and not sequential

## Slide 32: Memory
HDD are non volatile
The new version of ROM are not just readable anymore.
Modern computer hard disks are using Random Access
Tape Storage devices (used for offline backups) use Sequential Access.
https://sites.unica.it/dealab/organic-memories/
Notes: https://www.tech21century.com/sequential-vs-random-access-drives/

## Slide 33: Memory Hierarchy

## Slide 34: Self-Study

## Slide 35: Using The Memory Hierarchy
The goal is to access only the highest levels of the hierarchy
  On a miss, move down to the next level
    cache hit rates are as high as 98-99%
    misses happen in 1 to 2 of every 100 accesses
  Bring item up to higher level
  Bring its neighbors up as well in hopes of using them
Lower levels act as “backstops”
  On-chip caches are 32KB to 64KB today
  Off-chip cache might be as large as 8MB
  Main memory (DRAM) up to 8GB
  Use hard disk space for memory’s backstop, known as swap space or virtual memory
When something is not in memory
  Need to swap it from disk
  May require discarding something from memory

## Slide 36: Memory
• Storage of data and programs
• Ferrite cores (https://www.youtube.com/watch?v=HrlkEQvvxUA)
• RAM (Random Access Memory)
• ROM (Read Only Memory), PROM, EPROM, Flash-RAM
• «Virtual memory»
• Fast cache
• Level 1 - internal (on-die, on-chip); ~ KB
• Level 2 - internal / external; ~ MB
• Level 3 - externally ~ 10 MB
Notes: Other

## Slide 37: The Role of I/O
I/O – input and output
  All I/O takes place in the I/O subsystem
  Devices connect to computer by expansion cards and ports
Earliest form of I/O was punch cards (input) and printer (output) with magnetic tape used as intermediate storage
  No direct interaction with computer
Today, we expect to interact directly with the computer
  Pointing devices, keyboard, microphone, monitor, speakers
To improve interactivity, human computer interaction (HCI) combines
  Computer science
  Psychology
  Design
  Health
And ergonomics
  Reduce stress on the body (repetitive stress injuries very prevalent, particularly Carpal Tunnel Syndrome)
  Improve accessibility for people with handicaps through larger monitors, speech recognition, Braille output devices
  See for instance Rehabilitation Act section 508

## Slide 38: The Portable Computer
We no longer view the computer as a stationary device
  Laptops, notebooks
  Handheld devices
Recent and near-future I/O devices
  Wearables
  Touch screens
  Virtual reality interfaces
  Sensor networks
  Plug and play
With wireless access we have
  Interaction anywhere

## Slide 39: Tutorials
Personal Computer Architecture
https://www.youtube.com/watch?v=_I8CLQazom0&list=PLTd6ceoshprfg23JMtwGysCm4tlc0I1ou&index=2
(https://www.youtube.com/watch?list=PLTd6ceoshprfg23JMtwGysCm4tlc0I1ou&v=_I8CLQazom0&feature=emb_logo)

## Slide 40: CPU in Motherboard

## Slide 41: Motherboard
Connects:
  CPU
  Chipset
  Buses
  Memory tracks and RAM
  Expansion slots and extra cards
  Gates and «plugs»
a set of electronic components in an integrated circuit known as a "Data Flow Management System" that manages the data flow between the processor, memory and peripherals
Notes: the term chipset commonly refers to a set of specialized chips on a computer's motherboard
https://www.tomshardware.com/reviews/motherboard-parts-explained,5669.html

## Slide 42: Modern Motherboard: Connectors, Ports & Chipsets
1. CPU socket | 2. Chipset | 3. DIMM/RAM slots
4. PCIe x16 slot | 5. PCI x1 slot | 6. M.2 connector
7. SATA ports | 8. Front panel connectors | 9. USB 2. header
10. USB 3.1 Gen1 header | 11. USB 3.1 Gen2 header | 12. ATX power connector
13. CPU power connector | 14. BIOS chips | 15. CMOS battery
16. Fan headers | 17. Front panel header | 18. VRM heatsink
19. COM/Serial header | 20. TPM header | 21. RGB header
Asus Prime X470-Pro
DIMM (dual in-line memory module) slots are the place on your motherboard where the RAM goes
A PCIe x1 slot has one lane and can move one bit per cycle
X16 ideal for large and power hungry cards like a graphics card
To connect hard drives to motherboards
a ROM chip found on motherboards that allows you to access and set up your computer system at the most basic level
The BIOS is the program that starts a computer up, and the CMOS is where the BIOS stores the date, time, and system configuration details it needs to start the computer. ... CMOS is a type of memory technology, but most people use the term to refer to the chip that stores variable data for startup.
Voltage Regulator Thermal Module Pad
This slides is related to the harware.
You can self-read on canvas.
Notes: https://www.tomshardware.com/reviews/motherboard-parts-explained,5669.html
CMOS stands for “Complementary Metal Oxide Semiconductor.” The CMOS battery powers the BIOS firmware in your laptop [2]. BIOS needs to remain operational even when your computer isn't plugged into a power source. ... When your computer gets unplugged, BIOS relies on the CMOS battery for power.
COM (communication port) is the original, yet still common, name of the serial port interface on PC-compatible computers. It can refer not only to physical ports, but also to emulated ports, such as ports created by Bluetooth or USB adapters.

## Slide 43: End

## Slide 44: Lab assignment - Today
Review the lecture
  Get into groups of two-three
  Read and help each other to “Decode what is fetched” in the lecture time 
Work on your assignment on Metaverse,
  Find your group
  Choose your topic and some references
  Separate duties
Outcomes
  Practice the group work
  Learn for your exam